SysEx format for Lorenz.ptool
-----------------------------

 1 0xF0
 2 0x01
 3 'L'
 4 'r'
 5 'n'
 6 'z'
 7 delta * 1000 (14-bit)
 8
 9 s * 1000 (14-bit)
10
11 r * 1000 (14-bit)
12
13 b * 1000 (14-bit)
14
15 iterations (28-bit)
16
17
18
19 iteration count (28-bit)
20
21
22
23 tflags (tap=1; cycle=2; rhythm=4; spawn=8)
24 flags  (repeat=1; modify=4; make=8; match=16; valid=64)
25 match

/*** there is one of these for each output variable ***/
/*** X data is bytes 26-54, Y is 55-83, Z is 84-112 ***/

 1 'X' | 'Y' | 'Z'
 2 map (nada=0; time=1; dur=2; pitch=3; vel=4; ctrl=5; pbend=6; atouch=7; ptouch=8)
 3 controller number (valid if map==5);
 4 high -- range of 7-bit output data
 5 low
 6 beat_high (14-bit) -- range of time or duration output (valid if map==1 or 2)
 7
 8 beat_low (14-bit)
 9
10 output value (floating point value * 100000 packed into 28-bit format)
11
12
13
14 initial value (28-bit)
15
16
17
18 big value (28-bit)
19
20
21
22 small value (28-bit)
23
24
25
26 scalar (28-bit)
27
28
29

/************/


113 0xF7



Notes
		Values spread over two bytes (delta, s, r, b, beat_high, beat_low) are
		stored in MIDI unsigned 14-bit format yielding a range of 0 to 32,639.
		Integer fields that consume four bytes (iterations and iteration count)
		are stored in a MIDI-compatible unsigned 28-bit format with a range of
		0 to 2,139,062,143 (0x7F 0x7F 0x7F 0x7F).  Signed floating-point fields 
		(output, initial, big, small, scalar) are coerced into a 28-bit 
		MIDI-friendly format with a precision of five decimal places.  This format 
		supports a range of -10820.97535 to 10820.97535.  Bit 31 is the sign bit, 
		which indicates a negative number when set.  		
		
		The X, Y, and Z records are optional.  That is, you may have one, two, 
		three, or none of them in the sysex message.  
		
		Unless you really know what you are doing, do not mess with big, small, or
		scalar.  The Lorenz tool uses them internally when converting equation
		samples to event data.  You could really screw up things if you twiddle
		with them.  Also dangerous are the delta and constant s, r, and b values.
		Funky values in these fields can cause the equations to exceed machine
		infinity, which could result in a marginally interesting system crash.
				
		Of the most use are the iterations, iteration count, output, and initial 
		fields.  The Lorenz tool feeds the initial field value into the equations
		when it starts its cycle of equation calculations.  By selecting an 
		appropriate initial value and adjusting iterations and iteration count
		accordingly, you can loop the Lorenz equations through an arbitrary portion
		of the orbit.