[1mTonleitermeister Accessory[22m[0m


     [1mOverview[22m[0m   Tonleitermeister is an accessory for creating
                tuning map files for use with the Alternate
                Tuning tool.  Any combination of a note and
                pitch bend value may be mapped to a MIDI note
                number.  This accessory provides considerable
                latitude for experimenting with nonstandard
                equally-tempered tunings. 

     [1mControls[22m[0m   The functions of most of the gadgets in the
                Tonleitermeister window are duplicated in the
                accessory's two menus.  They are also available
                through key combinations.

                The Prev 12 and Next 12 gadgets page through the
                tuning map.  Twelve entries are displayed at a
                time in the Tonleitermeister window.  These
                commands are duplicated in the Options menu.

                The Ratios/Bends gadget toggles the display and
                edit mode of the output values.  In bend mode,
                the pitch class, octave, and cents of bend are
                displayed.  In ratio mode, real-number ratios
                (e.g. 1.500000) are displayed.

                The Numbers/Names gadget changes the display of
                input values, which are shown as either pitch
                class and octave, or MIDI note number.

                When selected, the Use Touched gadget causes a
                red (color 6) splotch to be displayed between
                the input and output values after a tuning table
                entry has been edited.  If Use Touched is
                selected when the Extrapolate gadget is hit,
                only entries that have been edited will be
                considered when the tuning map is computed.  If
                you save a tuning map while Use Touched is
                selected, unedited entries are marked invalid in
                the tuning file, and the Alternate Tuning tool
                disregards these entries.  This means that a
                user-defined tuning does not necessarily have to
                define an output for all MIDI note number
                values.  Use Touched is duplicated in the
                Options menu.

                The Clear Tuning gadget resets the tuning table
                to equal temperament.  This function is
                duplicated in the Tonleitermeister Project menu.

                The Extrapolate gadget clones one octave (as
                defined by the Divisions gadget) of tuning data
                into all other valid MIDI octaves, making
                necessary transpositions at octave boundaries.

                You can grab a tuning previously loaded into an
                Alternate Tuning tool with the Import Tuning
                gadget.  Select the desired tuning from the
                pop-up menu that is displayed when you click on
                the gadget.  After importing a tuning, it may be
                edited like any other.

                The Open Tuning... and Save Tuning... gadgets
                read and write tuning files.  These functions
                are duplicated in the Tonleitermeister Project
                menu.  By default the extension for a tuning
                file is "tun".

                The Root gadgets set the starting point for a
                tuning.  Depending on the state of the Show
                Numbers/Show Names gadget, the root is displayed
                as either a pitch class and octave, or a MIDI
                note number.

                The Divisions gadget sets the number of
                divisions per octave for a tuning.  This value
                is used to generalize an octave of data over the
                MIDI note range.


      [1mEditing[22m[0m   For each MIDI note number in the "IN" column,
                you may define an output value.  The output
                value may be defined as a pitch class, octave,
                and cents of bend, or as a ratio relative to the
                Root of the tuning.  Pitch class and octave
                values are edited via pop-up menus; bend is a
                string gadget.  Bend values are limited to ±99
                cents (for a larger bend you ought to call the
                output what it really is anyway).  Ratios are
                edited in string gadgets, and may be entered in
                any of three formats:  real numbers (e.g.
                1.500000), over and under values (e.g. 3/2), or
                regular B-flat ratios (e.g. 3:2).  All of these
                input formats are converted to the closest
                floating point representation.  Note that, due
                to the vagaries of floating point arithmetic,
                rounding errors will occur occasionally.  Rest
                assured that rounding, not truncation, is done
                so you get the least erroneous approximations
                for your ratios.


  [1mFile Format[22m[0m   This is the format of a tuning file (for
                whatever strange reason it might interest you).

             -----------------------------------------------------
             type data                       size (bytes)
             -----------------------------------------------------
             long 'TOON'                       4
             long fileSize                     4
             long 'DOPT'                       4
             long doptSize                     4
             long dopts                        4
             long 'NAME'                       4
             long nameSize                     4
             char name[]                       nameSize (variable)
             long 'PTAB'                       4
             long ptabSize                     4
             char rootpitch                    1
             char rootoctave                   1
             struct PitchDef pitchtable[128]   384 (128 3-byte  
                                                  records)
             ---- optional stuff (ratios) ----
             long 'RATS'                       4
             long ratSize                      4
             char ratios[ptabSize][RATCHARS]   ratSize (1536
                                                        bytes)
             -----------------------------------------------------